## Slide 1: Battery Modeling with Degradation Using Various Techniques Research Presentation
Jihoon Moon
Texas Tech University
September 24, 2021
Notes: Good afternoon. My name is Jihoon Moon
The topic of my research presentation today is ‘Battery Modeling with Degradation using various techniques.

## Slide 2: Table of Contents
Introduction
Basics of the Lithium-Ion Battery
  Battery Cell Charge/Discharge Dynamics
The Lithium-Ion Battery Model
  Single Particle Model (SPM)
  Degradation Model
  Finite Difference Method (FDM)
  Linearization Method
  Nonlinear Method
Results
Conclusion
Future Work
References
Notes: This presentation is divided into 7 parts. Introduction, Basics of the Lithium-ion battery, The lithium-Ion battery model, results, conclusions, Future work and references.

## Slide 3
1. Introduction
Modeling
Simulation
Analysis
→ In this presentation, the battery cell model with degradation using Finite Difference method is developed. Various methods to model the battery degradation is proposed to figure out how the negative surface concentration behaves under various inputs.
1
Notes: Let’s start with the introduction. In this presentation, the objective of this research is lithium-ion battery modeling and simulation.
The battery cell model with degradation model using Finite Difference method is developed.
And see how the negative surface concentration
and side reaction current density behave
under certain initial conditions depending on the Input current.

## Slide 4
2. Basics of the Lithium-ion Battery
Battery Cell Charge/Discharge Dynamics
The major components of Battery Cell
Positive Electrode
Negative Electrode
Electrolyte
Separator
Current Collector
Charge: Lithium ions deintercalate from Neg. Electrode and intercalate into Pos. Electrode
Discharge: Lithium ions deintercalate from Pos. Electrode and intercalate into Neg. Electrode
2
Battery Cell Components
Notes: Next is the Basics of the Lithium-ion Battery.
First, I’ll talk about the components of the battery cell.
As you can see in the Figure (click), there are five major components of the Battery cell. Positive electrode, Negative electrode, electrolyte, Separator and current collector.
Base on this composition I’ll explain the battery cell charge and discharge dynamics.
During the battery charge, the lithium-ions deintercalate from positive electrode’s particles and move through the electrolyte and then intercalate to the negative electrode’s particles. During this process, separator prevents electrons from flowing directly through electrodes and the current is produced depending on the electrons go through the external circuit. From these consequences, the voltage difference occurs between the electrodes. Also, the opposite occurs during discharge. This can be modeled as a spherical diffusion process which I will explain afterward.

## Slide 5
Single Particle Model (SPM)
3. The Lithium-ion Battery Model
The single-particle model (SPM) is used to represent the electrochemical dynamics, and solid-electrolyte interphase (SEI) layer growth represents capacity loss and resistance growth dynamics.
Major assumptions of the SPM
Electrodes are composed of spherical particles with a uniform current distribution.
Electrolyte Concentration () is constant.
Limitation
Inadequate to capture accurately the battery dynamics at high current rates due to the assumption of uniform electrolyte concentration. [1]
→ SPM is a simplification of the electrochemical model. This consequently reduces the computational cost and can describe the internal electrochemical states of the battery.
3
[1] I. Oyewole 2019
Single Particle Model of Lithium-Ion Battery
Notes: The third part of the presentation is the lithium-ion battery model.
In my research, I used the single particle model on the lithium-ion battery.
Single Particle model is a common type of physics-based model which is a simplification of 1D formulation for a lithium-ion battery that is suitable for real-time applications.
Also, it is used to represent the electrochemical dynamics and solid-electrolyte interphase layer growth which represents capacity loss and resistance growth.
There are major assumptions of the SPM to adapt to the battery.
First, it assumes that the electrodes are composed of spherical particles with a uniform current distribution.
Second it assumes that the electrolyte dynamic is neglectable.
This means that the electrolyte concentration is a constant value.
As you can see the figure (click), single particle model composed of two spherical models which represents the negative electrode and positive electrode.
Of course, there is a limitation of the single particle model that it is inadequate to capture accurately the battery dynamics at high current rates due to the assumption of uniform electrolyte concentration.
However, as I explained before, the single particle model is a simplification of the electrochemical model so that it consequently reduces the computational cost and can describe the internal electrochemical states of the battery.

## Slide 6
3. The Lithium-ion Battery Model
Spherical diffusion equation
→ The process of lithium ions intercalating and deintercalating from the electrodes is
represented by spherical diffusion
Single Particle Model (SPM)
Current Density
Butler-Volmer equation
4
relates to the loss of active material to the SEI layer
Notes: In the previous slides, one of the assumptions in the single-particle model was each electrode is composed of spherical particle.
For the case of a spherical particle, the intercalation of lithium ions in the solid phase is modeled as a process due to diffusion. Diffusion governs the concentration within each electrode expressed as the spherical diffusion equation with two boundary conditions which are at the center of the sphere and surface of the sphere.
Each electrode produces a voltage that depends nonlinearly on the surface concentration of that respective electrode.
The nonlinear function is the reference potential of the electrode for the positive electrode, and for the negative electrode.
The difference in potentials between the electrolyte and the electrodes drives the current through the battery. The Butler-Volmer equation expresses how this potential difference relates to the current.
As I said before in the introduction slide, one of the objectives of this presentation is to figure out how much degradation occurred in the battery cell. So as you can see in the negative electrode current density equation (click) there is a side reaction current density (click) which is one of the important variables in the degradation that relates to the loss of active material to the sei layer. I’ll explain this in detail next further slides
So based on the spherical diffusion equation and current density equation we could derive the surface concentration by using various techniques.

## Slide 7
Anode (-)
Cathode (+)
electrolyte
SEI Layer
3. The Lithium-ion Battery Model
Degradation Model
Battery degradation occurs by several mechanisms such as lithium plating, fracturing, and the Solid Electrolyte Interphase (SEI) layer.
The SEI layer is formed on the Anode surface by occurring the side reaction with lithium-ions and electrolytes.
5
growth
Active material loss
Resistance of the film layer increase
The layer formed on the Cathode is relatively smaller than the Anode layer
Single Particle Model of Lithium-Ion Battery with SEI layer
Notes: In this slide I'll explain about the battery degradtion.
Battery degradation occurs by several mechanisms such as lithium plating, fracturing and solid electrolyte interphase layer.
We focused on the degradation causes by sei layer growth that formed on the Anode surface (click) by occurring the side reaction with lithium ions and electrolyte.
The sei layer which typically forms at the negative electrode during recharging makes battery lose the lithium which is the most common and fundamental source of capacity fade in Lithium-ion battery.
So, if the sei layer thickness is getting thicker, the battery cell loses the active material, the internal impedance of the battery would increase, and the resistance of the film layer would increase.
Of course, the sei layer formed on the cathode. However,(click) it is relatively smaller than the anode layer so I focused on the degradation of the anode.

## Slide 8
3. The Lithium-ion Battery Model
Degradation Model
Side reaction current density
Resistance of the film layer
Growth of the film thickness
Rate of change of capacity loss
relates to , and
6
Notes: The equations in this slide are the formula of the degradation dynamics.
As I explained before, the first equations, (click) side reaction current density is the one of the important variable in the battery degradation from the sei layer.
The side reaction current density provides information regarding both the degradation rate and the overall degradation level
which means that it provides the total loss in cyclable Li-ions, which is an electrochemical measure of the capacity loss across the whole battery and over time.
As you can see from the Resistance of the film layer, Growth of the film thickness and Rate of change of capacity loss equations which are important parameters of the degradation process (point the three equations), we could know that these three equations are related with side reaction current density.

## Slide 9
3. The Lithium-ion Battery Model
Degradation Model
Algebraic expression for Side reaction current density
7
→ is determined as above equation algebraically by using overpotential equations which is a function of negative surface concentration () and input current ().
→
Notes: To figure out the side reaction current density through the simulation and to figure out the negative surface concentration in the battery cell with degradation by using the side reaction current density
we should solve the side reaction current density as a function of surface concentration and current from the bulter volmer equation.
So the final algebraic expression for side reaction current density which we solved is this equation (click) it is determined algebraically by using overpotential equations and negative reference potential equations.
This complex non-linear equation is combined with the battery cell model which is modeled by the finite difference method. I’ll explain this in detail next further slides.

## Slide 10
3. The Lithium-ion Battery Model
Finite Difference Method (FDM)
Finite Difference Method (FDM) is applied to the governing equation to convert the PDE into ODE to solve numerically.
→ FDM is used to model the battery system with a degradation model to discretize the electrode particle to compute concentration distribution.
8
…
Spherical particle radius discretized evenly.
Central-Difference Method is used to solve spherical diffusion equation.
→ The boundary conditions at and are applied
…
Discretized single particle electrode
Notes: Based on the battery dynamics I have been explained, I will explain how I modeled the battery cell.
As I explained briefly in the previous slides, I used the finite difference method to model the battery cell.
So in my research, FDM is applied to the spherical diffusion equation to covert the Partial differential equations into ordinary differential equations to solve numerically.
To be specific, FDM is used to model the battery system to discretize the electrode particle to compute concentration distribution.
In this process, Central difference in FDM is used to convert the complex PDEs of the spherical diffusion equation into ODEs which are expressed as the time derivative of lithium-ion concentration at each node as you can see this equation (click)
and applied the boundary conditions at the center of the particle and surface of the particle However, when you see the boundary condition at the surface of the particle (click), current density exists which contains the side reaction current density in the anode.

## Slide 11
3. The Lithium-ion Battery Model
Finite Difference Method (FDM)
Notice
To combine the degradation model into the battery system, the complex non-linear equation of should substitute into the battery model.
→ I am going to apply the two methods to coupled and battery model.
9
Linearization Method: the complex non-linear equation of is linearized
Nonlinear Method: Newton-Raphson Method is applied.
Remind
Notes: When I explained about the battery degradation as the sei layer growth in the negative electrode, I explained that total current density is the summation of the current density and side reaction current density.
However, remind that (click) Js is a complex nonlinear equation.
To substitute the boundary condition into the battery model got from the finite difference method, we should consider how to combine this complex nonlinear equation to the battery model.
So, I applied two methods to solve this problem.
First is, linearize the Js equation
and Second is, substitute this whole equation and solve numerically by using newton Raphson method.
I’ll explain this one by one.

## Slide 12
3. The Lithium-ion Battery Model
Linearization Method
To combine the complex nonlinear side reaction current density equation with the state-space model, equation is linearized.
The negative surface concentration equation is calculated based on the boundary condition at .
→
10
Notes: First, I’ll explain linearization method.
To combine the complex non-linear side reaction current density equation with state-space model, equation is linearized which is expressed as this equation(click)
and then substitute into the surface concentration equation.(click).
So, the Negative surface concentration equation (click) is the function of c sub n,N-1 which is the concentration just before the surface,
current and the coefficient of the linearized Js equation.
Based on these equations, we could figure out the negative surface concentration and side reaction current density with time.
우선 Linearization method를 설명하겠다. To combine the complex non-linear side reaction current density equation (𝐽_𝑠) with state-space model, 𝐽_𝑠 equation is linearized and then substitute into the surface concentration equation which is expressed as this equation. So, the Negative surface concentration equation is the function of 𝑐_(n,𝑁−1) which is the concentration just before the surface, current and the coefficient of the linearized Js equation. Based on these equations, we could figure out the negative surface concentration and side reaction current density with time.

## Slide 13
3. The Lithium-ion Battery Model
Nonlinear Method
First, discretized ODEs of concentration are calculated at each time step.
The negative surface concentration equation
Numerical analysis is required to solve the ODEs obtained from the finite difference method without using the linearized equation.
Too complicated to solve
11
Notes: Next is how I applied the Js equation directly to figure out the surface concentration at negative electrode.
As we know that Js is really complex nonlinear equation so that another Numerical analysis is required to solve the ODEs obtained from the finite difference method without using the linearized equation.
The first thing I did is discretize the ordinary differential equations as this equation (click) to figure out the concentration
at each time step.
Based on this equation and initial conditions, we could get the next time step of concentration notated as k (click)
from the previous time step of concentration notated as k-1 (click).
Next, we should get the negative surface concentration by using the concentration data. However, you can see that the negative surface concentration equation contains total negative current density.
It is too complicated to solve surface concentration, and also it is hard to solve analytically, so we need another numerical method as I explained before.
Next is how I applied the Js equation directly to figure out the surface concentration at negative electrode. As we know that Js is really complex nonlinear equation so that another Numerical analysis is required to solve the ODEs obtained from the finite difference method without using the linearized 𝐽_𝑠 equation.
가장 먼저 discretized ODE를 delta t를 활용하여 (파란색 박스 공식을 가르키면서) 이식과 같이 concentration 을 at each time step 마다 구할수 있도록 바꿨다.
초기상태를 기반으로 우리는 notation k 로 표현된 다음 타임스텝의 concentration 을 k-1으로 표현된 이전 타임스템을 통해 구할수 있게 된다. 그 다음 각 노드에서의 concentration 을 통해 우리는 negative surface concentration equation 을 구해야 하지만 이식을 보게 된다면 Jn이 있다. Csn 의 root 를 구하기에는 Jn이 굉장히 복잡하기 때문에 아까 설명했듯이 또다른 Numerical method가 필요하다.

## Slide 14
3. The Lithium-ion Battery Model
Nonlinear Method
Newton-Raphson Method
Newton-Raphson Method enables to find a better approximation of root through iteration at each time step.
12
Newton-Raphson Method iteration [2]
[2] commons.wikimedia
Notes: To troubleshoot this problem, the numerical method we applied
is newton Raphson method.
As you can see in the figure, newton Raphson method finding the root through the iteration work. In the same way as this, in our battery system, we find a better approximation of root which is the surface concentration through iteration at each time step.
우리가 이문제를 해결하기위해 적용한 Numerical method는 newton Raphson method다. As you can see the figure, 반복을 통해서 root를 구하는 것을 볼수있다. 우리 배터리시스템에서는 Newton-Raphson Method enables to find a better approximation of root 〖(𝑐〗_(𝑠,𝑛,𝑘,𝑝)) through iteration at each time step.
그 결과 우리는 각 시간에서의 surface concentration을 구할수 있었다.

## Slide 15
3. The Lithium-ion Battery Model
Nonlinear Method
13
Initial condition
()
&
Input current ()
FDM
We get
Newton-Raphson Method
Get the better approximation root () through iteration() at
Get next time step of
(at +1)
Notes: To explain this process more easily
I made a simple flow chart.
By using the initial condition of concentration and input current
we get the concentration at all nodes which are discretized inside the sphere of the electrode by using the finite difference method at t = k
And then we substitute the concentration data at N-1 which is just before the surface
into Newton Raphson Method function to get the better approximation root through iteration at t equal to k.
I set the number of iterations equal to 10 because the surface concentration converges before 10 iterations.
And then I get the side reaction current density.
After that, the code repeat this process to get the next time step of surface concentration and side reaction current density.
우리가 이문제를 해결하기위해 적용한 Numerical method는 newton Raphson method다. As you can see the figure, 반복을 통해서 root를 구하는 것을 볼수있다. 우리 배터리시스템에서는 Newton-Raphson Method enables to find a better approximation of root 〖(𝑐〗_(𝑠,𝑛,𝑘,𝑝)) through iteration at each time step.
그 결과 우리는 각 시간에서의 surface concentration을 구할수 있었다.

## Slide 16
3. The Lithium-ion Battery Model
Nonlinear Method
Due to iteration work to find at each time step, it was not an efficient way in terms of simulation time.
Based on the Newton-Raphson Method algorithm, we calculated the negative surface concentration
14
→ Solution Map allows us to skip iteration to find negative surface concentration.
by using the range of concentration which is already known as
And then make a solution map.
Solution map for
Notes: However, we know that this is not an efficient way in terms of simulation time due to iteration work to find surface concentration at each time step.
This research is to figure out the battery degradation which means that we need a long-time simulation.
So based on the newton Raphson method algorithm, we calculated the negative surface concentration (click) which is the function of the initial value of surface concentration and cn,N-1 and current by using the range of concentration which is already known as this (click). After that if you see the figure, I made a solution map by using input current and C sub N-1. This map gave us a solution to solve the degradation modeling nonlinearly.
Also, Solution Map allows us to skip iteration to find negative surface concentration. This means that if we input the concentration data got from the finite difference method and input current, we can figure out the surface concentration directly. This allowed us to greatly reduce the simulation time.

## Slide 17
4. Results
Simulation Condition
Input Current
15
State of Charge (SOC)
0.5
Time Range
24 (1 days)
Time Range
Output | Negative surface concentration | Side reaction current density
Output |  | 
→ Comparison between Linearization and Nonlinear Method
Notes: Before moving on to the results part, I’ll explain the simulation condition.
I implemented the input current in two cases
I equal to zero and sin wave.
And I set the initial condition SOC equal to 0.5.
And the time range I have been simulated is 24 hours.
So, I am going to show you the comparison result between linearization method and nonlinear method of the negative surface concentration and side reaction current density with time.

## Slide 18
4. Results
Input current = 0
Time = 24 hours (1 days)
SOC = 0.5
Linearization Method VS Nonlinear Method
16
VS Time
VS Time
Notes: First, I’ll show you the results at Input current equal to 0 at SOC=0.5 of the initial condition.
if you look at a plot on the left side, you can see that the negative surface concentration is decreasing with time and the Linearization method and Nonlinear method of this results show a similar trend. Also, if you look at the plot on the right side, you can see that the side reaction current density is increasing with time.

## Slide 19
4. Results
Input current = sin wave ()
Time = 24 hours (1 days)
SOC = 0.5
Linearization Method VS Nonlinear Method
17
VS Time
VS Time
Notes: Second is the results at I equal to sine wave
As you can see that other conditions are same as before.
We can also figure out that there is no big difference between linearization method and nonlinear method.
As you can see the side reaction current density plot, it shows quite difference between two methods however, when you see the y axis the scale is 10 to the minus sixth power so that we could know that it is really small difference between them.
I tried to figure out degradation by repeating charging and discharging through a sine wave.

## Slide 20
4. Result
 | Linearization Method | Nonlinear Method
Surface concentration value at t = 24 hours |  | 
Negative Concentration Variation |  | 
 | Linearization Method | Nonlinear Method
Surface concentration value at t = 24 hours |  | 
Negative Concentration Variation |  | 
19
→ To verify the model working properly, I calculated how much surface concentration changes at the negative electrode where degradation can be seen.
At input current (I) = 0
→ The gap between two methods is increasing with time.
vs time
Comparison result between Linearization (LM) and Nonlinear Method (NM)
Notes: So, let's compare with two methods.
If you look at the table (click), I calculated how much surface concentration changes at the negative electrode where degradation can be seen to verify the model working properly. Change of negative concentration was nearly same between the linearization method and nonlinear method.
However, if you look at the plot on the right side (click), I plot the gap between the two method of the side reaction current density data. The amount is really small, but we can figure out that it is increasing with time. It means that the battery degrades more in the nonlinear case.

## Slide 21
5. Conclusion
20
Basics of the Lithium-Ion Battery
Single Particle Model and Degradation
Finite Difference Method
Solution for degradation modeling
Notes: Now let’s move on to the conclusion part.
Let me wrap up the main points of the presentation. I explained about the main components of the lithium-ion battery and charge and discharge dynamics. And then I explained about the lithium ion battery modeling based on the single particle model and also explained about the mechanisms of degradation from the SEI layer and side reaction current density.
After that I show how we model the battery by using the finite difference method and suggested the two methods to combined the degradation into the battery model.

## Slide 22
5. Conclusion
20
Simulation Result
Solution Map for Nonlinear method
Notes: And I suggested the solution map that it is new way to solve the surface concentration more easily by using the newton Raphson method.
Lastly, based on this battery model, I presented and analyzed the simulation results.

## Slide 23
6. Future Work
Objective: Get a reduced-order model of the battery dynamics
Full model
Reduced Order Model
(ROM)
u
Objective function ()
GA function
  Pade Approximation: No good due to nonlinearity
  Optimization-based model reduction → I am now applying the Genetic Algorithm.
21
Options
[A], [B],
[C], [D]
Genetic Algorithm
Notes: Moving on to the last section, I’d like to explain about future work briefly.
Currently, I am working on the reduced order modeling of the battery dynamics. The objective of the battery modeling that I did so far is to get the reduced order model.
There are few options of reduced order modeling method I considered to apply.
First was the Pade approximation. However, due to nonlinearity it was hard to get the transfer function.
So I am now working on the genetic algorithm which is one of the optimization-based model reduction methods to get the reduced order model of the battery.
To briefly explain this method, based on the design variables, we generate the initial population and then we calculate the objective function for the fitness function.
After that, we gonna generate the genetic algorithm function such as the selection, crossover, mutation process until it converges to the best option we can get.

## Slide 24
7. References
[1] I. Oyewole, “Optimal Model Reduction of Lithium-Ion Battery Systems Using Particle Swarm Optimization”, Master’s Degree thesis submitted to University of Michigan-Dearborn, 2019.
[2] “File:NewtonIteration Ani.gif,” Wikimedia commons, Sept 04. 2005, https://commons.wikimedia.org/wiki/File:
NewtonIteration_Ani.gif.
[3] ﻿D. J. Docimo and H. K. Fathy, “Analysis and control of charge and temperature imbalance within a lithium-ion battery pack,” IEEE Trans. Control Syst. Technol., 2018.
[4] ﻿ D. J. Docimo and H. K. Fathy, “Using a Linear Quadratic Regulator to Attenuate Cell-to-Cell Heterogeneity within a Lithium-Ion Battery Pack,” in IEEE Conference on Control Technology and Applications (CCTA), 2018, pp. 1935–1402.
[5] D. Zhang, S. Dey, and S. J. Moura, “Lithium-ion battery state estimation for a single particle model with intercalation-induced stress,” in Annual American Control Conference (ACC), pp. 2294–2299, IEEE, 2018.
[6] D. J. Docimo, “Insights into the Behavior of Heterogeneous Thermostatically Controlled Loads and Battery Packs.”, 2017.
[7] D.J. Docimo and H. K. Fathy, “Multivariable state feedback control as a foundation for lithium-ion battery pack charge and capacity balancing,” J. Electrochem. Soc., vol. 164, no. 2, pp.A61-A70, 2017.
[8] D. J. Docimo, M. Ghanaatpishe, and H. K. Fathy, “Development and experimental parameterization of a physics-based second-order lithium-ion battery model” in Proc. ASME Dyn. Syst. Control Conf., 2014, p. V001T19A003.
Notes: So, this is the end of the presentation and thanks for listening.

## Slide 25
Thank you for listening!
Notes: So, this is the end of the presentation and thanks for listening.